## Slide 1: COP 3402 Systems Software
Euripides Montagne
University of Central Florida

## Slide 2: COP 3402 Systems Software
Assemblers

## Slide 3: ISA Instruction descriptions
opcode mnemonic meaning
0001 LOAD <x> A  Mem[x]
0010 ADD <x> A  A + Mem[x]
0011 STORE <x> Mem[x]  A
0100 SUB <x> A  A – Mem[x]
0101 IN <Device_#> A  read from Device
0110 OUT <Device_#> A  output to Device
0111 HALT Stop
1000 JMP <x> PC  x
1001 SKIPZ If Z = 1 Skip next instruction
1010 SKIPG If G = 1 Skip next instruction
1011 SKIPN If L = 1 Skip next instruction

## Slide 4: Assembly language Programming examples
Assign a memory location to each variable:
C  X + Y;
<000> <001> <002>
If necessary to use temporary memory locations,
assign labels (names) to them.

## Slide 5: Assembly language Programming examples
Memory
000 1245
001 1755
002 0000
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
Memory
000 1245
001 1755
002 3000
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
After execution

## Slide 6: One Address Architecture
The instruction format of this one-address architecture consists of 16 bits: 4 bits to represent instructions and 12 bits for addresses :
OP
ADDRESS
0001
0000 0001 0001

## Slide 7: Assembler: translate Symbolic code to object code(binary)
Assembly Language
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
003 0001 0000 0000 0000
004 0010 0000 0000 0001
005 0011 0000000000011
006 0111 0000000000000
In binary
01  LOAD 06  OUT
02  ADD 07  HALT
03  STORE 08  JMP
04  SUB 09  SKIPZ
05  IN
Assembler

## Slide 8: Assembler Directives
The next step to improve our assembly language is the incorporation of pseudo-ops (assembler directives) to invoke a special service from the assembler (pseudo-operations do not generate code)
.begin  tells the assembler where the program starts
.data  to reserve a memory location.
.end  tells the assembler where the program ends.
Labels are symbolic names used to identify memory locations.

## Slide 9: Assembler Directives
This is an example of the usage of assembler directives
.begin
“Assembly language instructions”
halt (return to OS)
.data (to reserve a memory location)
.end ( tells the assembler where the program ends)
note:
the directive .end can be used to indicate where the program
Starts (for eample: “.end <insert label here>”

## Slide 10: Assembly language Programming Example 1
Label opcode address
start .begin
in x005
store a
in x005
store b
load a
sub TWO
add b
out x009
halt
a .data 0
b .data 0
TWO .data 2
.end start
Data section
Text section (code)

## Slide 11: Assembly language Programming Example 2
Label opcode address
01 ; This is
02 ; a comment
03 start .begin x200
04 here LOAD sum
05 ADD a
06 STORE sum
07 LOAD b
08 SUB one
09 STORE b
0A SKIPZ
0B JMP here
0C LOAD sum
0D HALT
0E sum .data x000
0F a .data x005
10 b .data x003
11 one .data x001
12 .end start
This program is computing
5 x 3.

## Slide 12: ASSEMBLER Pass 1
Label opcode address
01 ; This is
02 ; a comment
03 start .begin x200
04 here LOAD sum x200
05 ADD a x201
06 STORE sum x202
07 LOAD b x203
08 SUB one x204
09 STORE b x205
0A SKIPZ x206
0B JMP here x207
0C LOAD sum x208
0D HALT x209
0E sum .data x000 x20A
0F a .data x005 x20B
10 b .data x003 x20C
11 one .data x001 x20D
12 .end start x20E
Symbol Table
here x200
sum x20A
a x20B
b x20C
one x20D
symbol address
In pass one the assembler examines
the program line by line in order to
built the symbol table.
There is an entry in the symbol table
for each label found in the program.

## Slide 13: Opcode and Symbol Tables
opcode mnemonic
0001 LOAD
0010 ADD
0011 STOR
0100 SUB
0101 IN
0110 OUT
0111 HALT
1000 JMP
1001 SKIPZ
1010 SKIPG
1011 SKIPN
Symbol Table
here x200
sum x20A
a x20B
b x20C
one x20D
symbol address
Using the symbol table and the
opcode table the assembler
translates the program to object
code.
As the program can be loaded
anywhere in memory PC-relative
addressing is used to resolve
the symbols.
Opcode table
For instance, the offset between LOAD sum and the
declaration of sum is 9, because when LOAD sum
is fetched for execution, the pc is pointing to the
instruction ADD a. ( pc + offset = 9)

## Slide 14: ASSEMBLER Pass 2
Label opcode address
01 ; This is
02 ; a comment Object code
03 start .begin x200
04 here LOAD sum x200 0001000000001001 (9 is the offset)
05 ADD a PC x201 0010000000001001
06 STORE sum x202 0011000000000111 (7 is the offset)
07 LOAD b x203 0001000000001000
08 SUB one x204 0100000000001000
09 STORE b x205 0011000000000110
0A SKIPZ x206
0B JMP here x207
0C LOAD sum x208
0D HALT x209
0E sum .data x000 x20A
0F a .data x005 x20B
10 b .data x003 x20C
11 one .data x001 x20D
12 .end start x20E
All addresses are
pc-relative addresses.
(PC + offset)
Recall: PC is always pointing to
the next instruction to be fetch.
o
f
f
s
e
t

## Slide 15: Assembly language Programming object code
Label opcode address
01 ; This is
02 ; a comment Object code
03 start .begin x200
04 here LOAD sum x200 0001000000001001 (9 is the offset)
05 ADD a PC x201 0010000000001001
06 STORE sum x202 0011000000000111 (7 is the offset)
07 LOAD b x203 0001000000001000
08 SUB one x204 0100000000001000
09 STORE b x205 0011000000000110
0A SKIPZ x206 1001000000000000
0B JMP here x207 1000111111111000 (-7)
0C LOAD sum x208 0001000000000001
0D HALT x209 0111000000000000
0E sum .data x000 x20A 0000000000000000
0F a .data x005 x20B 0000000000000101
10 b .data x003 x20C 0000000000000011
11 one .data x001 x20D 0000000000000001
12 .end start x20E
o
f
f
s
e
t
One’s complement

## Slide 16: ASSEMBLER object code
The object code file has several sections:
Header section: Size of code, name source file, size of data
Text section (code): Object code
Data section: Data (in binary)
Relocation information section: Addresses to be fixed up by the linker
Symbol table section: Global symbols in the program, Imported symbols
Debugging section: Source file and line number information, description of
data structures.

## Slide 17: ASSEMBLER object code file for the example
Program name: start
Starting address text: x200
Length of text in bytes: x14
Starting address data: x20A
Length of data in bytes: 8
0001000000001001
0010000000001001
0011000000000111
0001000000001000
0100000000001000
0011000000000110
1001000000000000
1000111111111000
0001000000000001
0111000000000000
0000000000000000
0000000000000101
0000000000000011
0000000000000001
Header
Text section
Data section

## Slide 18: Loading Object code in Memory
Program name: start
Starting address text: x200
Length of text in bytes: x14
Starting address data: x20A
Length of data in bytes: 8
0001000000001001
0010000000001001
0011000000000111
0001000000001000
0100000000001000
0011000000000110
1001000000000000
1000111111111000
0001000000000001
0111000000000000
0000000000000000
0000000000000101
0000000000000011
0000000000000001
Header
Text section
Data section
Run time environment
Text
Data
Stack
Heap
Object code file (disk)

## Slide 19: UNIX a.out format
a.out header
text section
data section
symbol table information
relocation Information
a.out header
magic number
text segment size
initialized data size(data)
uninitialized data size(bss)
symbol table size
entry point
text relocation size
data relocation size
a.out object code format
magic number indicates type of executable file.
bss is an acronym for block storage start.
entry point: starting address of the program
a.out stands for "assembler output".

## Slide 20: COP 3402 Systems Software
THE END